## Slide 1
WISI GT34 / PRTG
Monitoring Scope Report
What the system monitors — carriers, multiplexes, DVB services, parameters and operational meaning
4
WISI chassis
43
TV-bearing carrier inputs
168
DVB service instances
Production checkpoint V11.3L • Authoritative Inventory V6

## Slide 2
Executive monitoring scope
Current authoritative scope; earlier HTML snapshot is used as a presentation reference, not as the current count baseline.
4
WISI chassis / IRDs
8
GT34 modules
43
logical carrier / multiplex inputs
43
distinct frequency + polarization combinations
168
DVB service instances
What “43 multiplexes” means
Each monitored logical carrier/input is a tuned RF carrier carrying one or more DVB services. A multiplex can therefore contain several television, radio or other DVB services.
What “168 services” means
168 is the authoritative V6 count of service instances across the monitored carriers. It is not the same as 168 separately licensed TV channels; feeds, variants, radio and other DVB services may be included.
What is actually alarmed
Carrier lock, transport-stream presence and expected-service integrity are monitored. Individual expected services can alarm even while their carrier remains locked and the multiplex is otherwise present.
Scope hierarchy: 4 chassis → 8 GT34 modules → 43 logical RF carriers/multiplexes → 168 DVB service instances

## Slide 3
Fleet coverage by chassis
All four production WISI chassis are part of the monitoring fleet.
PRTG label | Chassis IP | GT34 modules | Authoritative active carriers
WISI-IRD-01 | 192.168.3.27 | M1 + M5 | 11
WISI-IRD-02 | 192.168.3.45 | M1 + M5 | 9
WISI-IRD-03 | 192.168.3.8 | M1 + M5 | 16
WISI-IRD-04 | 192.168.3.9 | M1 + M5 | 7
43 total logical carrier inputs
The final PRTG deployment has one production sensor per authoritative TV-bearing logical carrier.

## Slide 4
RF and multiplex scope
Every authoritative production carrier currently has a distinct frequency/polarization combination.
43
distinct RF frequency/polarization combinations
43
monitored logical multiplex/carrier inputs
1 : 1
current carrier-to-frequency/polarization count
Frequency
The satellite downlink frequency tells the IRD where the RF carrier is located. Monitoring it confirms that the sensor is associated with the intended transponder/carrier rather than an arbitrary tuner.
Polarization + Symbol Rate
Polarization (H/V) separates satellite signal planes. Symbol rate describes how quickly symbols are transmitted and is a key tuning fingerprint. Together with frequency, it helps identify the intended carrier deterministically.
Important: the project distinguishes physical module/tuner identity from the WISI GUI logical input identity.

## Slide 5
Service-level monitoring scope
A multiplex is not treated as healthy merely because its RF carrier is locked.
168
expected DVB service instances
43
TV-bearing multiplex/carriers
6
Geo services on M1C10
15 days
service/carrier history
Expected service
A service identified by SID that should exist inside a monitored multiplex. If an expected SID disappears, the system treats it as a service-integrity fault.
Elementary-stream evidence
Where available, the IRD exposes video/audio PID and elementary-stream information. This is used to prove that a carrier is TV-bearing and to assess service integrity.
Other services
The monitored DVB inventory can include radio/audio-only, feeds, variants and services whose ES metadata is unavailable. These are tracked as DVB services; they are not automatically counted as separately licensed TV channels.

## Slide 6
What does “total channels” mean?
Three different counts must not be mixed.
43 monitored carrier sensors
Operational PRTG scope. One final sensor represents one authoritative TV-bearing logical carrier/multiplex. This is the number of production carrier monitoring points.
168 DVB service instances
Technical service scope. These are expected service occurrences across all multiplexes. The same service may appear more than once and some entries can be radio, feeds or variants.
Unique TV channel count
A refreshed unique regulatory-TV count is not asserted from V6 alone. The earlier attached scope snapshot reported 125 unique confirmed video services, but it represented an earlier 38-carrier / 167-instance scan and is therefore not used as the current authoritative total.
For management reporting today: use 43 monitored multiplexes and 168 DVB service instances. Do not label all 168 as licensed TV channels.

## Slide 7
Core technical parameters monitored
17 core parameter/health categories are prioritized on every carrier sensor.
Parameter | Plain-language meaning
Carrier / TS Health | Overall “is the reception path usable?” indicator.
Demod Lock | Whether the IRD can lock onto the satellite carrier.
Transport Stream Present | Whether usable DVB data is arriving after demodulation.
Video Present | Whether video evidence is available for the TV-bearing carrier.
Service Integrity Health | Whether all expected services are present and structurally observable.
RF Level | Strength of the received radio-frequency signal.
SNR | How clearly the wanted signal stands above noise.
BER | How many received bits are erroneous; lower is better.
Frequency | Where the satellite carrier is tuned.
Symbol Rate | Transmission symbol speed; part of carrier identity.
TS Bitrate | Rate of the digital transport stream.
TSID | Identifier of the DVB transport stream.
NID | Identifier of the DVB network.
ONID | Original Network ID used to identify the originating DVB network.
Missing Services | Expected SIDs that are not currently present.
Unexpected Services | New/unexpected SIDs seen on the multiplex.
ES Metadata Unavailable | Expected service exists, but elementary-stream details cannot currently be obtained.

## Slide 8
Beyond the 17 core parameters
PRTG is deliberately bounded; the richer technical observation is preserved elsewhere.
44 max
live PRTG channels per sensor
17
always-prioritized core categories
15 days
full SQLite observation history
Additional PRTG channels
Where room exists, per-service health and aggregates such as discovered/running/expected services, ES totals, video/audio counts, modulation/FEC enums and MIS are included.
Rich status text
Overflow detail remains visible in sensor status: configured/detected modulation & FEC, PLS/ISI, LNB/IF, network/providers, service SIDs, PIDs and stream types, where the IRD exposes them.
SQLite history
Full carrier and expected-service observations are stored for 15 days. The database is the historical record; PRTG channels are the bounded visual/operational surface.

## Slide 9
How monitoring turns into an alarm
The system distinguishes a whole-carrier failure from an individual service failure.
1. Carrier unlocked
The IRD cannot lock the RF carrier. All services on that multiplex are treated as DOWN.
2. TS absent
RF may be locked, but no usable transport stream is present. All multiplex services are treated as DOWN.
3. Service integrity
Carrier and TS are up, but one expected SID is missing or its ES metadata is unavailable. Only that service alarms.
Immediate notification
Python sends the Transmission Alert immediately. There is no 60-second debounce and no repeated email while the same episode remains active.
Immediate recovery
When the notified condition clears, Python sends the corresponding UP/recovery message and records total downtime.
PRTG notification triggers are not used for production email; Python remains authoritative.

## Slide 10
What the project gives the regulator
A layered view from satellite RF health down to individual DVB service integrity.
Continuous coverage of 4 WISI chassis and 8 GT34 modules.
43 authoritative TV-bearing logical carrier/multiplex monitoring points across 43 distinct frequency/polarization combinations.
168 expected DVB service instances monitored inside those multiplexes.
17 core RF/TS/service-integrity parameter categories prioritized on every sensor, with up to 44 live PRTG channels per sensor.
Rich modulation, FEC, service, PID/ES and network detail retained in sensor status and SQLite where exposed by the IRD.
15-day carrier/service history for technical review and incident analysis.
Immediate, duplicate-suppressed alarm and recovery email controlled by Python.
Evidence-based service classification: the system does not infer TV/radio status merely from a service name.
Monitoring scope = RF carrier health + DVB transport health + expected-service integrity + historical evidence

## Slide 11
Important interpretation note
The attached HTML report is a valuable earlier live-scan snapshot, but its counts predate the final authoritative V6 migration.
Earlier attached scope snapshot
38 production carrier/input instances
33 distinct RF frequency/polarization combinations
167 expected DVB service instances
158 confirmed video service instances
125 unique confirmed video services
4 unique audio-only services
1 unique data/unknown service
3 unique unavailable services
Current authoritative project scope
43 production logical carrier/multiplex inputs
43 distinct RF frequency/polarization combinations
168 expected DVB service instances
All 43 carriers proven TV-bearing at carrier level
Service-integrity monitoring retained for all expected services
Current unique video/audio split should be regenerated from a fresh fleet classification before publishing a new unique-channel total.
This presentation therefore uses V6 for current scope and uses the attached HTML only for historical classification context.